## Slide 1: The Functional Mock-up Interface 3.0 Beginners’ Tutorial

## Slide 2: Agenda
Intri
Motivation / History
How does FMI work?
Tool support
New features in FMI 3.0
Overall agenda
Times
Q&A after each sections

## Slide 3
Motivation, Timeline
“Why FMI”?
“And how did it develop”

## Slide 4: Motivation
  Define a tool-independent, free-to-use standard for exchange and co-simulation of models between different simulation tools
  Provide models in a containerized form
  Decouple Know-How between producers and users of FMUs
  Decouple know-how between different brands engineers and software programmers
  Massive Re-use of modelling investment
  IP Protection

## Slide 5: Timeline : Modelisar Project  Modelica Association Project FMI
FMI 1.0 (and most part of FMI 2.0) was developed in the publicly funded project Modelisar
2008-2011: MODELISAR project
2011: Release of FMI 1.0
2012: Foundation of MAP FMI as a project in the Modelica Associations
Members: see FMI Webpage
2013: Release of FMI 2.0 --> focus of this tutorial
2021: Release of FMI 3.0

## Slide 6: Versioning of FMI
FMI uses semantic versioning:
Major releases
non backwards or forward compatible changes
e.g. „FMI 2.0.4“
Minor releases
Can introduce new features
FMI 3.1 is planned to be the first minor release
Backwards compatibility „FMI 3.0 will be valid FMI 3.1 FMUs“
Bugfix/Maintenance releases
No new features, only bugfixes and clarifications possible
Backwards and forward compatibility

## Slide 7
FMI: Technical Fundamentals
“How does FMI work?”

## Slide 8: Exporting vs. importing tool
The FMI standard decouples authoring and execution tool / toolchain / environment
ASCMO
Cruise
FMU SDK
Simplorer
Silver
ModelFit
COSYM
TLK TISC
CarMaker®
Simplorer
VEOS
INCA Flow
By TLK
export as Functional Mockup Unit (FMU) accordingg to the FMI Standard
develop model
FMI
import FMU
(co-)simulate model / run model somewhere else
Exporting tool
Importing tool
Remove icons

## Slide 9: The FMI standard
The FMI Standard defines the “Functional Mock-up Interface” FMI, an interface between a model and a simulation environment.
It consists of the definition of
  a C-API (application programming interface)
  an interface description (modelDescription.xml) according to a defined schema
  the definition of an exchangeable unit, an “FMU” (Functional Mock-up Unit), technically a zip file

## Slide 10
FMI deals with the interface and does not define a CS-Algorithm
the homepave.
(Sentence from the homepage)

## Slide 11: Models in scope
ODE: ordinary differential equations
Algebraic relations
Algorithms
Continuous vs. Discrete
ODE Solver
Continuous system
ODEs, algebraic equations
Solver needed
Discrete parts
Notion of time (independent variable)

## Slide 12: Co-Simulation
Co-Simulation: (from the FMI 3.0.1 glossary)
Coupling of several simulation programs in order to compute the global behavior of a system that consists of several subsystems.
Subsystems are coupled in the sense that the behavior of each subsystem depends on the behavior of the remaining subsystems, so that the co-simulation must be computed in a step-by-step fashion.
Each simulation program is responsible for computing the behavior of a subsystem, using the outputs produced by the other simulation programs.
There can be an additional error introduced by the co-simulation, that has to limited to an acceptable size by using a suitable co-simulation algorithms and communication pattern (e.g. step size)

## Slide 13: FMU – „Functional Mock-up Unit“
A model container, that can be distributed
Technically it is realized a zip File, with ending „.fmu“
Content:
  modelDescripotion.xml: meta-data with information on the model variables, interface, capabilitis and to a limited extent model structure
  Model representation
    Binaries for one or multiple platforms and/or (“black box”)
    Source code (e.g C-Code)
  Optionally: Resources, documentation, Icons, port definitions
  /extra information (defined in layered standards)
myModel.fmu
model.dll
modelDescription.xml

## Slide 14: FMU for Model Exchange vs. Co-Simulation (FMI 2.0)
Model Exchange (ME)
  Importing tool provides the solver.
  Properties:
  Very tight integration of model in simulation tool
  Complex interface between importing tool and model
  Importing tool must provide a suitable solver for the model
  Used e.g. for inclusion of Modelica support in non-Modelica tools (using the solver of the the importing tool)
Co-Simulation (CS)
  Exporting tool provides the solver.
  Properties:
  Tight coupling of model and a suitable solver
  Simpler interface between importing tool and model
  Freedom in the selection of a co-simulation algorithm and communication timestep to reach a stable and accurate solution
  Used in most industrial applications
Tool
Solver
FMU
Model
Tool
FMU
Model
Solver

## Slide 15: Co-Simulation calling sequence
Communication timestep can be different from internal steps (e.g. Variable step solver)
Calling sequence CS
  Set inputs: fmi2SetXXX(...)
    Trigger calculation until next communication point: fmi2doStep(...)
    Get outputs: fmi2GetXXX(...)
For an implementation in C, see e.g. fmusimi in the Reference FMUs: https://github.com/modelica/Reference-FMUs/blob/main/fmusim/fmusim_fmi2_cs.c
You can view the calling sequence with fmusim --log-fmi-calls
Use 1.0 CS FMU Put the code there

## Slide 16: ME
Idea: similar to S-Function
Expose RHS of the ODEs
Use 1.0 CS FMU Put the code there

## Slide 17: FMI for Co-simulation Tool Wrapper Variant
Co-simulation stand-alone FMU
  self-contained FMU
Co-simulation FMI Tool Wrapper
  FMU dependent on an existing tool installation
Capabiltiy flag

## Slide 18: FMI tool support
https://fmi-standard.org/tools/: FMI supported by >= 180 Tools
Exporting tools
  Modeling and simulation tools
  Model-based software creation
  Wrapping of algorithms, virtual ECUs
  …
Importing tools
  Modeling and simulation tools
  Co-simulation tools and integration platforms
  Implementations for programming and scripting languages
  ….

## Slide 19: Compatibility information
Replaces the cross-check that helped to improve he maturity of FMI 1.0 and 2.0 supporting tools.
Information on on how FMI export and import have been tested provided by the tool vendors and linked in the tools list
Tools providing compatibility information are marked with a golden star and listed on top of the tools list https://fmi-standard.org/tools/:

## Slide 20: Validation of FMUs

## Slide 21: Licenses and licensing
License information in documentation folder
Not covered by FMI standard
Legal

## Slide 22
New features with FMI 3.0

## Slide 23: Motivation for FMI 3.0
  180+ tools support FMI now: many users now, many new use-case requests:
  Virtual Electronic Control Units (vECUs):
    FMI 2.0 works well for physics simulations: better support for vECUs is needed
  Advanced Co-Simulation
    Co-Simulation is the more popular interface type: improved co-simulation methods are needed to improve performance and accuracy
  Multi-FMU simulations are getting more common
    Events are necessary in complex control systems
    Events must be synchronized across FMUs
  New ML and AI applications
    More derivatives computations is required
vECU
Co-Sim
Events
AI
API Efficiencies

## Slide 24: FMI 3.0: New Interface Type – Scheduled Execution
FMI 2.0
Model Exchange
Co-Simulation
FMI 3.0
Model Exchange
Co-Simulation
Scheduled Execution
Scheduled Execution allows coupling several FMUs with one, external scheduler (OS)
vECU
Events
Notes: This is necessary for collaborative development of complex system controllers

## Slide 25: FMI 3.0: Main Improvements
New Application
Performance
Accuracy
    Event mode for Co-Simulation
    Intermediate variable update
    Clocks
    New variable types
    Array variables
    Terminals and icon
    FMI for Scheduled Execution (SE)
    Preparation for layered Standards
Notes: Show co-sim and intermediate output notebooks

## Slide 26: Layered Standards
Extension mechanism ….

## Slide 27: Resources
FMI Webpage
FMI tools list
FMU validation
Reference FMUs, fmpy, Jupyter notebooks
(Unofficial) Stack overflow (tagged FMI)
(Unofficial) FMI LinkedIn Group
Linkd

## Slide 28
Example model for hands-on part

## Slide 29: Example model: Controlled Motor Drive
Motor Drive with PI control –> FMU-Export
Model created in Modelica, with tool Dymola (also SimulationX, …)
Load Step
at time 0,5s
Desired torque
Step at time 0,1s
Drive FMU
Control FMU
Stimuli FMU
Reference solution
Angular speed
------------------
DEMO
------------------
Overall FMU
Only slide

## Slide 30: Backup

## Slide 31: FMI Standard & FMI support in tools
Modelica Association Project FMI
FMI Design Group Members
All members have signed the MAP FMI’s CCLA (corporate contributor license agreement)
FMI Standard
FMI specifications: CC-BY-SA 4.0 (Creative Common Attribution-ShareAlike 4.0 International)
Source code (C-header & XML-schema files): 2-Clause BSD License7
Layered Standards
(domain specific extensions ot the FMI Standard)
Tool Vendors
have freedom to choose their licensing model
FMU import / export might be free
FMU export might require a license FMU might require runtime license (FlexLMSee also
License conditions and legal aspects
Layered Standards
(domain specific extensions ot the FMI Standard

## Slide 32: FMI: Simpler „Plumbing“ for Simulation
  FMI for Model Exchange: How to connect systems of equations (ODEs)
  FMI for Co-Simulation: How to connect “any” model or tool
  Decouple Know-How between producers and users of FMUs
  Decouple know-how between different brands engineers and software programmers
  Massive Re-use of modelling investment
  Many new use-cases are now viable
  150+ tools now support FMI: See: fmi-standard.org/tools
https://fmi-standard.org/

## Slide 33: FMU for Model Exchange vs. Co-Simulation (FMI 2.0)
Model Exchange (ME)
  Importing tool provides the solver.
  Pros:
    Typically more stable as the solver gets direct access to the entire set of equations (internal modules and FMUs).
  Cons:
    Importing tool must have rich set of solvers that are able to properly handle the imported FMU (stiff, variable step size, event handling, parse,…).
Co-Simulation (CS)
  Exporting tool provides the solver.
  Pros:
    Exporting tool can apply the most appropriate solver.
    Typically faster for large systems.
    Well suited for parallelization and multi-rate integration.
  Cons:
    Numerical stability cannot be guaranteed.
    Performance depends on master algorithm (communication step size, events, interpolation).
    Master algorithm depends on the maturity of the FMUs.
Tool
Solver
FMU
Model
Tool
FMU
Model
Solver

## Slide 34: Motivation
  Digital Mock-up (DMU) for packaging is state of the art in industry:
  Suppliers deliver geometry of their components as CAD data
  OEMs assemble them to the whole virtual system
  Added value:
  Check consistency of parts
  Computation of design envelope
  Evaluation of assemblability and disassemblability
How to include behavior in mockup?
Source: Teraport GmbH

## Slide 35: FMU Structure and Content
FMU implements FMI
FMU = .zip-file with renamed file extension
Must include modelDescription.xml (I/O description + some info)
Must include at least one binary representation or source code
Some optional content:
XML schema (.xsd)
defined by the
FMI specification
.fmu
model.dll
Solver
GUI
<<read>>
<<control>>
<<run>>
1..*
modelDescription.xml
<<references>>
Functional Mock-up Unit

## Slide 36: History
      The FMI 1.0 was developed in 2008-2011 by initiative of DAIMLER in the EU-0funded MODELISAR project with participation of OEMs, tool vendors and research institutes.
FMI defines an interface for the model exchange between different simulation tools and development partners (e.g., OEMs <-> supplier)

## Slide 37
FMI: Technical Fundamentals
“How does FMI work?”

## Slide 38: The FMI standard
The FMI Standard defines the “Functional Mock-up Interface” FMI, an interface between a model and a simulation environment.
It consists of
  a C-API (application programming interface)
  an interface description (modeldescription.xml) according to a defined schema
  the definition of an exchangealble unit, an “FMU” (Functional Mock-up Unit), technically a zip file

## Slide 39: FMU Structure and Content
FMU implements FMI
FMU = .zip-file with renamed file extension
Must include modelDescription.xml (I/O description + some info)
Must include at least one binary representation or source code
Some optional content:
XML schema (.xsd)
defined by the
FMI specification
.fmu
model.dll
Solver
GUI
<<read>>
<<control>>
<<run>>
1..*
modelDescription.xml
<<references>>
Functional Mock-up Unit

## Slide 40: FMU for Model Exchange vs. Co-Simulation (FMI 2.0)
Model Exchange (ME)
  Importing tool provides the solver.
  Pros:
    Typically more stable as the solver gets direct access to the entire set of equations (internal modules and FMUs).
  Cons:
    Importing tool must have rich set of solvers that are able to properly handle the imported FMU (stiff, variable step size, event handling, parse,…).
Co-Simulation (CS)
  Exporting tool provides the solver.
  Pros:
    Exporting tool can apply the most appropriate solver.
    Typically faster for large systems.
    Well suited for parallelization and multi-rate integration.
  Cons:
    Numerical stability cannot be guaranteed.
    Performance depends on master algorithm (communication step size, events, interpolation).
    Master algorithm depends on the maturity of the FMUs.
Tool
Solver
FMU
Model
Tool
FMU
Model
Solver

## Slide 41
Unterschied Schrittweite bei CS : Communication timestep, internal
Calling sequence CS
SetXX
doSTEP
GetXX
(Code von RefFMUs kopieren)
https://github.com/modelica/Reference-FMUs/blob/main/fmusim/fmusim_fmi2_cs.c
Set Input, doStep, Sample (get output)
Calling sequence fmusim --log-fmi-calls (verkürzen)

## Slide 42: FMI for Co-simulation Tool Wrapper Variant
Co-simulation stand-alone FMU
  self-contained FMU
Co-simulation FMI Tool Wrapper
  FMU dependent on an existing tool installation

## Slide 43: (Co-)Simulation of multiple FMUs
Numerical Solver (ME) or Co-Simulation Algorithm (CS)
or
Scheduler (SE)
Not defined by FMI!
Functional Mock-up Interface
Exported by: Tool 1
Tool 2
Tool 3
Tool n
…
FMU
FMU
FMU
FMU

## Slide 44: Limitations of FMI
Loss of Information
  Partitioning of overall system
  IP protection (Intention of FMI) vs. need to reveal info for in-house application
  Unstructured signal interface (only scalars; no physical connectors) 3.0
  Unsorted list of parameters (no hierarchies/groupings; dependencies hidden) layered standard?
FMI addresses ‘only’ interface problem, not numerical problem
  Partitioning of system numerically difficult for tight couplings
  Coupling & master algorithms not defined
Importing / Exporting
  Maturity of FMI support varies between importing and exporting tools.
  If something goes wrong, then who is responsible the exported FMU, the importing tool, the combination?
Properties of FMI
Black box

## Slide 45: ToDo
FMI and licenseing
Resources
FMI Checking

## Slide 46: New in FMI 3.0

## Slide 47: Motivation for FMI 3.0
  170+ tools support FMI now: many users now, many new use-case requests:
  Virtual Electronic Control Units (vECUs):
    FMI 2.0 works well for physics simulations: better support for vECUs is needed
  Advanced Co-Simulation
    Co-Simulation is the more popular interface type: improved co-simulation methods are needed to improve performance and accuracy
  Multi-FMU simulations are getting more common
    Events are necessary in complex control systems
    Events must be synchronized across FMUs
  New ML and AI applications
    More derivatives computations is required
vECU
Co-Sim
Events
AI
API Efficiencies

## Slide 48: FMI 3.0: Main Improvements
New Application
Performance
Accuracy
    Event mode for Co-Simulation
    Intermediate variable update
    Clocks
    New variable types
    Array variables
    Terminals and icon
    FMI for Scheduled Execution (SE)
    Preparation for layered Standards
Notes: Show co-sim and intermediate output notebooks

## Slide 49: FMI 3.0: New Interface Type – Scheduled Execution
FMI 2.0
Model Exchange
Co-Simulation
FMI 3.0
Model Exchange
Co-Simulation
Scheduled Execution
Scheduled Execution allows coupling several FMUs with one, external scheduler (OS)
vECU
Events
Eigenschaften: External Schduler
Notes: This is necessary for collaborative development of complex system controllers

## Slide 50: FMI 3.0: New Data Types
FMI 1.0, FMI 2.0 | FMI 3.0 | Remarks
fmiReal | fmi3Float32 | Discrete and continuous variables
 | fmi3Float64 | States, derivatives, event-indicators
fmiInteger | fmi3Int8, fmi3UInt8 | Discrete variables
 | fmi3Int16, fmi3UInt16 | 
 | fmi3Int32, fmi3UInt32 | 
 | fmi3Int64, fmi3UInt64 | 
fmiBoolean | fmi3Boolean | char
fmiString | fmi3String | const char* ('\0' terminated, UTF-8 encoded)
 | fmi3Binary | const char* (e.g. sensor outputs, bitmaps, …)
 | fmi3Clock | Transport information about events
vECU
Notes: Simple: these data types are used in real ECUs, having them in FMI enables realistic vECUs
Also: binary data for video, Lidar, radar, whever you want Modelica channel: tool demos

## Slide 51: Array Variables (Vectors, Matrices, …)
FMI 1.0 and FMI 2.0:
  Naming convention for array elements (building.room.temp[0], building.room.temp[1], …)
  Array elements are treated as scalars, one valueReference for each variable
FMI 3.0:
  Variables can have multiple <Dimension> elements
  Each dimension can be:
    Constant: specified by <start> attribute
    Changeable: depends on a structural parameter which can change its value only in Configuration or Reconfiguration Mode
  fmi3SetXXX, fmi3GetXXX work on whole arrays
vECU
API Efficiencies

## Slide 52: Terminals & Icons
  Terminals group input and output variables to Terminals, which represent buses or physical connectors
  Predefined matching rules (plug, bus, sequence) for the whole Terminal, other rules are possible
  FMI Terminals are not acausal! The causality (input, output) is defined by the referenced variable!
Much improved UI: same structure & closer visual appearance to real system
Notes: Use case: build UIs that reflect the structure of the physical system, or as in Modelica

## Slide 53: FMI for Co-Simulation: Event Handling
  Introduction of Event Mode like in Model Exchange
  Event Mode can be entered by the importer:
    to handle input events triggered outside the FMU
    on request of the FMU
  fmi3DoStep(…) can return before communicationStepSize is reached if an FMU internal event needs to be treated outside
  Capability flag hasEventMode signals if event handling is supported by the FMU
  Argument eventModeUsed of fmi3InstantiateCoSimulation signals if event handling is supported by the importer
Co-Sim
Events
Demo in a Jupyter Notebook binder: Performance & Accuracy trade-offs, comparison FMI 2.0 vs. FMI 3.0

## Slide 54: FMI for Co-Simulation: Intermediate Variable Access
  FMI1/2 CS: FMUs exchange values only at communication points.
  FMI3.0: allows information exchange between the FMU and the master also at intermediate time points
  Realized with an extension to the state machine: Intermediate update mode which can be entered by the FMU via the callback function fmi3CallbackIntermediateUpdate(…) at arbitrary times out of fmi3DoStep(…)
  This enables various use cases:
    Advanced co-simulation algorithms using interpolation / extrapolation techniques
    Transmission Line Modeling (TLM) co-simulation
    Input approximation similar to what is possible in FMI 2.0
    More detailed plotting of simulation results (using additional time point)
Co-Sim
Demo in a Jupyter Notebook binder: Performance & Accuracy trade-offs, comparison FMI 2.0 vs. FMI 3.0

## Slide 55: Clocks
  Clocks synchronize FMUs with the importer and with other FMUs:
    Clocks carry the information that a specific event happens
    Clocked variables belong to one clock (a so-called clocked model partition). They change only if this clock is active.
  Clocks allow precise handling of time events (independent from continuous time: fmi3SetTime(), or arguments of fmi3DoStep())
  In Scheduled Execution Communication Clocks are used:
    by the importer to identify the specific partition which is to be executed
    by the FMU to announce, which model partition wants to be scheduled
vECU
Co-Sim
Events

## Slide 56: Clock Types
Clock Type |  | causality | interval | Example
Time-based | periodic clock | input | constant | Clocked PI-controller with a defined constant interval
 |  |  | fixed | Clocked PI-controller, interval is defined by periodic fmi3SetClock calls
 |  |  | calculated | Clocked PI-controller, interval is defined by fixed parameter(s) of the FMU
 |  |  | tunable | Clocked PI-controller, interval is defined by tuneable parameter(s) of the FMU
 | aperiodic clock | input | changing | Simulation of the behaviour of a control algorithm with non constant execution time, Generation of pulse sequences
 |  |  | countdown | Time delayed action after an event, for example ignition signal some time after crankshaft angle event
Triggered |  | input | triggered | Control algorithm, triggered by a crankshaft angle sensor
 |  | output | triggered | Crankshaft angle sensor which ticks several times per revolution
vECU
Co-Sim
Events

## Slide 57: Adjoint Derivatives
In several applications, including backpropagation for gradient-based training AI models, adjoint derivatives (“vector gradient products" (VJPs)) are needed
They can be implemented efficiently using revers mode automatic differentiation (AD)
FMI 3.0 provides now two access functions for partial derivatives:
Benefit:
This will allow to more efficiently encapsulate and train AI models with FMI
Connection of the Python/Julia tool world of AI to the system simulation world
Enabling the combination of physics-based and AI-based models (e.g. neural ODEs) and training in a unified framework
AI

## Slide 58: Concept of Layered Standard
  The layered standard concept allows the specification of standards on top of FMI
  XML element annotations and strings allow additional semantic for variables and terminals
  Extra folder in FMU zip-file allows shipping of additional files at a well-defined place without disturbing compatibility
  Examples:
    XCP: When packaging virtual electronic control units (vECUs), XCP allows standardized access (see ASAM) to ECU internal variables (in preparation on FMI GitHub)
    Network2Signals: Allows grouping and description of FMU inputs and outputs as network signals (in preparation on FMI GitHub)
    Including of 3D-Visualization to FMUs which represent multi body simulation models (prototype from ESI ITI and TU Dresden)
vECU
Notes: Demo available. Not necessarily important to show.

## Slide 59: Miscellaneous
  Graphical representations for the whole FMU and for Terminals can be defined (Icons)
  Alias variable names are now specified by a list of alias names for each variable and no longer by a separate variable with the same valueReference.
  Dependencies might change at runtime due to variable structure of the model or due to changes of array sizes. Dependencies for (array) variables can now be retrieved at runtime.
  Asynchronous execution of fmi2DoStep was removed for simplification. This feature was never used and can be implemented by the importer.
  Improvement and clarification of source code FMUs for better platform independency.

## Slide 60
https://fmi-standard.org/tools/
Kategorisierung von tools import / import

## Slide 61: Compatibility information
Replaces cross-check

## Slide 62: Licenses ..
Not covered by FMI standard
Enforcement
Legal

## Slide 63
  Resources:
    Main website: https://fmi-standard.org/
    Development process can be tracked on GitHub: https://github.com/modelica/fmi-standard
    FMI Layered Standards: https://github.com/modelica/fmi-ls-xcp; https://github.com/modelica/fmi-ls-bus
    FMPy is permanently updated to support FMI 3.0: https://github.com/CATIA-Systems/FMPy
    Reference FMUs: https://github.com/modelica/Reference-FMUs

## Slide 64: Example model: Controlled Motor Drive
Motor Drive with PI control –> FMU-Export
Model created in Modelica, with tool Dymola (also SimulationX, …)
Load Step
at time 0,5s
Desired torque
Step at time 0,1s
Drive FMU
Control FMU
Stimuli FMU
Reference solution
Angular speed
------------------
DEMO
------------------
Overall FMU

## Slide 65: More information
Web site: https://fmi-standard.org
Tool list: https://fmi-standard.org/tools/
    Ask your tool vendors!
Publications: https://fmi-standard.org/literature/
Open-source tool kits:
  Many more use cases:
    Reference FMUs: more example FMUs
    FMPy: Python integration, validation
Links
FMI Example notebooks