## Slide 1: The Functional Mock-up Interface 3.0 Beginners’ Tutorial

## Slide 2
Motivation, History, Organizational & Legal Aspects of FMI

## Slide 3: Fundamental idea
The FMI standard decouples authoring and execution tool / toolchain / environment
ASCMO
Cruise
FMU SDK
Simplorer
Silver
ModelFit
COSYM
TLK TISC
CarMaker®
Simplorer
VEOS
INCA Flow
By TLK
export as Functional Mockup Unit (FMU) by adding the FMI
develop model / code somewhere
FMU
import FMU
(co-)simulate model / run code somewhere else

## Slide 4: Motivation
  Digital Mock-up (DMU) for packaging is state of the art in industry:
  Suppliers deliver geometry of their components as CAD data
  OEMs assemble them to the whole virtual system
  Added value:
  Check consistency of parts
  Computation of design envelope
  Evaluation of assemblability and disassemblability
How to include behavior in mockup?
Source: Teraport GmbH

## Slide 5: History
      The FMI 1.0 was developed in 2008-2011 by initiative of DAIMLER in the EU-0funded MODELISAR project with participation of OEMs, tool vendors and research institutes.
FMI defines an interface for the model exchange between different simulation tools and development partners (e.g., OEMs <-> supplier)

## Slide 6: Modelica Association & Tool Vendors
Modelica Association Project
FMI Design Group Members
All members have signed the MAP FMI’s CCLA (corporate contributor license agreement)
FMI Standard
FMI specifications: CC-BY-SA 4.0 (Creative Common Attribution-ShareAlike 4.0 International)
Source code (C-header & XML-schema files): 2-Clause BSD License7
Layered Standards
(domain specific extensions ot the FMI Standard)
Tool Vendors
have freedom to choose their licensing model
FMU import / export might be free
FMU export might require a license (e.g. Dymola)
FMU might require runtime license (FlexLMSee also
License conditions and legal aspects
Layered Standards
(domain specific extensions ot the FMI Standard

## Slide 7
FMI technology

## Slide 8: The FMI standard
The FMI Standard defines the “Functional Mock-up Interface” FMI, an interface between a model and a simulation environment.
It consists of
  a C-API (application programming interface)
  an interface description (modeldescription.xml) according to a defined schema
  the definition of an exchangealble unit, an “FMU” (Functional Mock-up Unit), technically a zip file

## Slide 9: FMU Structure and Content
FMU implements FMI
FMU = .zip-file with renamed file extension
Must include modelDescription.xml (I/O description + some info)
Must include at least one binary representation or source code
Some optional content:
XML schema (.xsd)
defined by the
FMI specification
.fmu
model.dll
Solver
GUI
<<read>>
<<control>>
<<run>>
1..*
modelDescription.xml
<<references>>
Functional Mock-up Unit

## Slide 10: (Co-)Simulation of multiple FMUs
Numerical Solver or Master Algorithm
Not defined by FMI!
Functional Mock-up Interface
Tool X
Tool Y
Tool Z
Tool n
…
FMU
FMU
FMU
FMU

## Slide 11: FMU for Model Exchange vs. Co-Simulation
Model Exchange (ME)
  Importing tool provides the solver.
  Pros:
    Typically more stable as the solver gets direct access to the entire set of equations (internal modules and FMUs).
  Cons:
    Importing tool must have rich set of solvers that are able to properly handle the imported FMU (stiff, variable step size, event handling, parse,…).
Co-Simulation (CS)
  Exporting tool provides the solver.
  Pros:
    Exporting tool can apply the most appropriate solver.
    Typically faster for large systems.
    Well suited for parallelization and multi-rate integration.
  Cons:
    Numerical stability cannot be guaranteed.
    Performance depends on master algorithm (communication step size, events, interpolation).
    Master algorithm depends on the maturity of the FMUs.
Tool
Solver
FMU
Model
Tool
FMU
Model
Solver

## Slide 12: FMI for Co-simulation Tool Wrapper Variant
Co-simulation stand-alone FMU
  self-contained FMU
Co-simulation FMI Tool Wrapper
  FMU dependent on an existing tool installation

## Slide 13: Limitations of FMI
Loss of Information
  Partitioning of overall system
  IP protection (Intention of FMI) vs. need to reveal info for in-house application
  Unstructured signal interface (only scalars; no physical connectors)
  Unsorted list of parameters (no hierarchies/groupings; dependencies hidden)
FMI addresses ‘only’ interface problem, not numerical problem
  Partitioning of system numerically difficult for tight couplings
  Coupling & master algorithms not defined
Importing / Exporting
  Maturity of FMI support varies between importing and exporting tools.
  If something goes wrong, then who is responsible the exported FMU, the importing tool, the combination?

## Slide 14: FMI 3.0: Main Improvements
New Application
Performance
Accuracy
    Event Mode for Co-Simulation
    Intermediate Variable Update
    Clocks
    New Types
    Array Variables
    Terminals and Icons
    FMI for Scheduled Execution
    Preparation for Layered Standards
Notes: Show co-sim and intermediate output notebooks

## Slide 15: FMI 3.0: New Interface Type – Scheduled Execution
FMI 2.0
Model Exchange
Co-Simulation
FMI 3.0
Model Exchange
Co-Simulation
Scheduled Execution
Scheduled Execution allows coupling several FMUs with one, external scheduler (OS)
vECU
Events
Notes: This is necessary for collaborative development of complex system controllers

## Slide 18: Motivation
Operator Training
Monitoring
Predictive Maintenance
Concept
Implementation
Design and Optimization
Architecture
Requirements
Executable Specification
UML
SysML
Component
FEM, CFD
MBS
Modelica
VHDL-AMS
Signal based
Model Predictive Control
Observers
Diagnostics
System
MBS
Modelica
VHDL-AMS
Signal based
MiL
SiL
HiL
VHiL
Model
Model
Model
Model
Model
Model
Test and Verification
Operation

## Slide 19: FMI: Simpler „Plumbing“ for Simulation
  FMI for Model Exchange: How to connect systems of equations (ODEs)
  FMI for Co-Simulation: How to connect “any” model or tool
  Decouple Know-How between producers and users of FMUs
  Decouple know-how between different brands engineers and software programmers
  Massive Re-use of modelling investment
  Many new use-cases are now viable
  150+ tools now support FMI: See: fmi-standard.org/tools
https://fmi-standard.org/

## Slide 20: Motivation for FMI 3.0
  170+ tools support FMI now: many users now, many new use-case requests:
  Virtual Electronic Control Units (vECUs):
    FMI 2.0 works well for physics simulations: better support for vECUs is needed
  Advanced Co-Simulation
    Co-Simulation is the more popular interface type: improved co-simulation methods are needed to improve performance and accuracy
  Multi-FMU simulations are getting more common
    Events are necessary in complex control systems
    Events must be synchronized across FMUs
  New ML and AI applications
    More derivatives computations is required
vECU
Co-Sim
Events
AI
API Efficiencies

## Slide 21: Models and model exchange along the “Design- Vee”
Requirements
Design
Validated system
vECU
Co-Sim
Co-Sim
AI
AI
Events
Events

## Slide 22: FMI 3.0: New Data Types
FMI 1.0, FMI 2.0 | FMI 3.0 | Remarks
fmiReal | fmi3Float32 | Discrete and continuous variables
 | fmi3Float64 | States, derivatives, event-indicators
fmiInteger | fmi3Int8, fmi3UInt8 | Discrete variables
 | fmi3Int16, fmi3UInt16 | 
 | fmi3Int32, fmi3UInt32 | 
 | fmi3Int64, fmi3UInt64 | 
fmiBoolean | fmi3Boolean | char
fmiString | fmi3String | const char* ('\0' terminated, UTF-8 encoded)
 | fmi3Binary | const char* (e.g. sensor outputs, bitmaps, …)
 | fmi3Clock | Transport information about events
vECU
Notes: Simple: these data types are used in real ECUs, having them in FMI enables realistic vECUs
Also: binary data for video, Lidar, radar, whever you want Modelica channel: tool demos

## Slide 23: Array Variables (Vectors, Matrices, …)
FMI 1.0 and FMI 2.0:
  Naming convention for array elements (building.room.temp[0], building.room.temp[1], …)
  Array elements are treated as scalars, one valueReference for each variable
FMI 3.0:
  Variables can have multiple <Dimension> elements
  Each dimension can be:
    Constant: specified by <start> attribute
    Changeable: depends on a structural parameter which can change its value only in Configuration or Reconfiguration Mode
  fmi3SetXXX, fmi3GetXXX work on whole arrays
vECU
API Efficiencies

## Slide 24: Terminals & Icons
  Terminals group input and output variables to Terminals, which represent buses or physical connectors
  Predefined matching rules (plug, bus, sequence) for the whole Terminal, other rules are possible
  FMI Terminals are not acausal! The causality (input, output) is defined by the referenced variable!
Much improved UI: same structure & closer visual appearance to real system
Notes: Use case: build UIs that reflect the structure of the physical system, or as in Modelica

## Slide 25: FMI for Co-Simulation: Event Handling
  Introduction of Event Mode like in Model Exchange
  Event Mode can be entered by the importer:
    to handle input events triggered outside the FMU
    on request of the FMU
  fmi3DoStep(…) can return before communicationStepSize is reached if an FMU internal event needs to be treated outside
  Capability flag hasEventMode signals if event handling is supported by the FMU
  Argument eventModeUsed of fmi3InstantiateCoSimulation signals if event handling is supported by the importer
Co-Sim
Events
Demo in a Jupyter Notebook binder: Performance & Accuracy trade-offs, comparison FMI 2.0 vs. FMI 3.0

## Slide 26: FMI for Co-Simulation: Intermediate Variable Access
  FMI1/2 CS: FMUs exchange values only at communication points.
  FMI3.0: allows information exchange between the FMU and the master also at intermediate time points
  Realized with an extension to the state machine: Intermediate update mode which can be entered by the FMU via the callback function fmi3CallbackIntermediateUpdate(…) at arbitrary times out of fmi3DoStep(…)
  This enables various use cases:
    Advanced co-simulation algorithms using interpolation / extrapolation techniques
    Transmission Line Modeling (TLM) co-simulation
    Input approximation similar to what is possible in FMI 2.0
    More detailed plotting of simulation results (using additional time point)
Co-Sim
Demo in a Jupyter Notebook binder: Performance & Accuracy trade-offs, comparison FMI 2.0 vs. FMI 3.0

## Slide 27: Clocks
  Clocks synchronize FMUs with the importer and with other FMUs:
    Clocks carry the information that a specific event happens
    Clocked variables belong to one clock (a so-called clocked model partition). They change only if this clock is active.
  Clocks allow precise handling of time events (independent from continuous time: fmi3SetTime(), or arguments of fmi3DoStep())
  In Scheduled Execution Communication Clocks are used:
    by the importer to identify the specific partition which is to be executed
    by the FMU to announce, which model partition wants to be scheduled
vECU
Co-Sim
Events

## Slide 28: Clock Types
Clock Type |  | causality | interval | Example
Time-based | periodic clock | input | constant | Clocked PI-controller with a defined constant interval
 |  |  | fixed | Clocked PI-controller, interval is defined by periodic fmi3SetClock calls
 |  |  | calculated | Clocked PI-controller, interval is defined by fixed parameter(s) of the FMU
 |  |  | tunable | Clocked PI-controller, interval is defined by tuneable parameter(s) of the FMU
 | aperiodic clock | input | changing | Simulation of the behaviour of a control algorithm with non constant execution time, Generation of pulse sequences
 |  |  | countdown | Time delayed action after an event, for example ignition signal some time after crankshaft angle event
Triggered |  | input | triggered | Control algorithm, triggered by a crankshaft angle sensor
 |  | output | triggered | Crankshaft angle sensor which ticks several times per revolution
vECU
Co-Sim
Events

## Slide 29: Adjoint Derivatives
In several applications, including backpropagation for gradient-based training AI models, adjoint derivatives (“vector gradient products" (VJPs)) are needed
They can be implemented efficiently using revers mode automatic differentiation (AD)
FMI 3.0 provides now two access functions for partial derivatives:
Benefit:
This will allow to more efficiently encapsulate and train AI models with FMI
Connection of the Python/Julia tool world of AI to the system simulation world
Enabling the combination of physics-based and AI-based models (e.g. neural ODEs) and training in a unified framework
AI

## Slide 30: Concept of Layered Standard
  The layered standard concept allows the specification of standards on top of FMI
  XML element annotations and strings allow additional semantic for variables and terminals
  Extra folder in FMU zip-file allows shipping of additional files at a well-defined place without disturbing compatibility
  Examples:
    XCP: When packaging virtual electronic control units (vECUs), XCP allows standardized access (see ASAM) to ECU internal variables (in preparation on FMI GitHub)
    Network2Signals: Allows grouping and description of FMU inputs and outputs as network signals (in preparation on FMI GitHub)
    Including of 3D-Visualization to FMUs which represent multi body simulation models (prototype from ESI ITI and TU Dresden)
vECU
Notes: Demo available. Not necessarily important to show.

## Slide 31: Miscellaneous
  Graphical representations for the whole FMU and for Terminals can be defined (Icons)
  Alias variable names are now specified by a list of alias names for each variable and no longer by a separate variable with the same valueReference.
  Dependencies might change at runtime due to variable structure of the model or due to changes of array sizes. Dependencies for (array) variables can now be retrieved at runtime.
  Asynchronous execution of fmi2DoStep was removed for simplification. This feature was never used and can be implemented by the importer.
  Improvement and clarification of source code FMUs for better platform independency.

## Slide 32: Roadmap & Resources
  FMI 3.0 has been published in May 2022. Due to continuous tool development and testing of prototypes, the quality of the standard is much higher than for standards where the definition and the prototyping are decoupled!
  Currently the development focuses on
    The implementers guide for FMI 3.0, nearly finished: https://modelica.github.io/fmi-guides/main/fmi-guide/
    And on “Layered Standards” on top of the final FMI 3.0 specification
    “Backporting” of some of the FMI 3.0 features to FMI 2.X as layered standards
  Resources:
    Main website: https://fmi-standard.org/
    Development process can be tracked on GitHub: https://github.com/modelica/fmi-standard
    FMI Layered Standards: https://github.com/modelica/fmi-ls-xcp; https://github.com/modelica/fmi-ls-bus
    FMPy is permanently updated to support FMI 3.0: https://github.com/CATIA-Systems/FMPy
    Reference FMUs: https://github.com/modelica/Reference-FMUs

## Slide 33: More information
Web site: https://fmi-standard.org
Tool list: https://fmi-standard.org/tools/
    Ask your tool vendors!
Publications: https://fmi-standard.org/literature/
Open-source tool kits:
  Many more use cases:
    FMUSDK: example FMUs and simple importer
    FMU Checker: validate your FMUs
    Reference FMUs: more example FMUs
    FMPy: Python integration