## Slide 1
FMI Applications
and Its Role in Digital Twins
Presenters:
Cinzia Bernardeschi, University of Pisa
Maurizio Palmieri, University of Pisa
Claudio Gomes, Aarhus University
Online Materials:
https://github.com/modelica/fmi-beginners-tutorial-2023/tree/main

## Slide 2: Autonomous Driving Advanced System (SW/HW co-simulation)
Model Predictive Control simulation on selected Hardware platform
Objective:
Validating the controller and assessing the adequacy of the hardware platform with respect to timing constraints and its performance
- GRAMPC
- VPSim - Armv8 Quad-core 64-bit
- Simulink
FMI role: easy validation of deployment of GRAMPC on a simulated architecture
C. Bernardeschi, P. Dini, et al. , Co-simulation of a Model Predictive Control System for Automotive Applications, SEFM 2021 Collocated Workshops, https://link.springer.com/chapter/10.1007/978-3-031-12429-7_15
http://www.european-processor-initiative.eu/ H2020, Grant Agreement No26647
CEA, List, France

## Slide 3: Multi-agent systems: aerial, land vehicles
Multi-UAV system: Planning & Control Objective:
Controller parameters (attitude and position control) calibration for stability in co-operative systems; optimality of values with respect to time to convergence and energy consumption
- Planning algorithm (logic language, python)
- Controller (C)
- Plant (Modelica)
FMI role:
Analysis of the relation between the numeric integration step (co-simulation step) and time discretization interval for planning for stability; analysis of optimality of control parameters value
- https://github.com/INTO-CPS-Association/example-linear-quadcopter - C. Bernardeschi, A. Domenici, et al., Co-simulation and Formal Verification of Co-operative Drone Control With Logic-Based Specifications The Computer Journal, vol. 66, Issue 2, 2023, https://doi.org/10.1093/comjnl/bxab161
Erle-robotics quadcopter
Voronoi tesselletion

## Slide 4: Human-centered systems
Integrated Clinical Environment (ICE)
User interaction with the realistic interfaces of the devices Easy testing and validation of device interaction from different manufactures (use error)
Devices: PVSioweb
Patient: OpenModelica
FMI role:
Validate ICE with respect to patient model. Formal proof of a use-related safety requirement of a device used in the co-simulation
M. Palmieri, C. Bernardeschi, P. Masci. A framework for FMI-based co-simulation of human–machine interfaces, Software and Systems Modeling, vol. 19, Issue 3, 2020, https://dl.acm.org/doi/abs/10.1007/s10270-019-00754-9

## Slide 5: Communications in connected vehicles
Platoon of land vehicles
V2V communication against centralized multi-access edge computing. Performance with vehicle dynamics and different road surface conditions. Strategies to drive safely a platoon in critical road conditions.
FMI role: swap from one network architecture to another; analysis of unsafe conditions
M. Palmieri, C. Quadri, et.al, Co-simulated Digital Twin on the Network Edge: the case of platooning, IEEE International Symposium on a World of Wireless, Mobile and Multimedia Networks, 2022, doi:10.1109/WoWMoM54355.2022.00096.
3-vehicles
platoon

## Slide 6: Other applications
P. Palensky, E. Widl, M. Stifter and A. Elsheikh, "Modeling Intelligent Energy Systems: Co-Simulation Platform for Validating Flexible-Demand EV Charging Management," in IEEE Transactions on Smart Grid, vol. 4, no. 4, pp. 1939-1947, Dec. 2013, doi: 10.1109/TSG.2013.2258050.
Gomes, Cláudio, Giuseppe Abbiati, and Peter Gorm Larsen. “Seismic Hybrid Testing Using FMI-Based Co-Simulation.” In Proceedings of the 14th International Modelica Conference. online: Linköping University Electronic Press, Linköpings Universitet, 2021. https://doi.org/10.3384/ecp21181287.
Pedersen, N., Lausdahl, et. al (2017). Distributed Co-Simulation of Embedded Control Software with Exhaust Gas Recirculation Water Handling System using INTO-CPS. In 7th International Conference on Simulation and Modeling Methodologies, Technologies and Applications (pp. 73–82).

## Slide 7: FMI & Digital Twins

## Slide 8: Definition in this Tutorial: Digital Shadow
Physical Twin (CPS)
Plant
Controller
Digital Shadow
Visualization
Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Communication
Env

## Slide 9: Digital Twin Definition in this Tutorial
Physical Twin (CPS)
Digital Twin
Visualization
Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Re-configuration of PT
Communication
Plant
Controller
Env

## Slide 10: Opportunities of FMI in DTs
Leverage design time models at deployment time.
Development
Deployment
Physical Twin
Digital Twin
Deploy models without design time tooling.

## Slide 11: Role of FMI in Digital Twinning
Digital Twin
Visualization
Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Re-configuration
Communication
Models
Laughman, Christopher, and Scott A Bortoff. “Nonlinear State Estimation with FMI: Tutorial and Applications,” 23–25, 2020.
Legaard, Christian Møldrup, Cláudio Gomes, Peter Gorm Larsen, and Frederik F. Foldager. “Rapid Prototyping of Self-Adaptive-Systems Using Python Functional Mockup Units.” In Proceedings of the 2020 Summer Simulation Conference, 1–12. SummerSim ’20. Virtual Event. https://doi.org/10.5555/3427510.3427532.
Bogomolov, Sergiy, Cláudio Gomes, Carlos Isasa, Sadegh Soudjani, Paulius Stankaitis, and Thomas Wright. “Reachability Analysis of FMI Models Using Data-Driven Dynamic Sensitivity.” SIMULATION, Special Issue: Engineering of Dependable Digital Twins, 2023, accepted.

## Slide 12: Thank you!
Presenter Contacts
Cinzia Bernardeschi cinzia.bernardeschi@unipi.it
Maurizio Palmieri maurizio.palmieri@ing.unipi.it
Cláudio Gomes claudio.gomes@ece.au.dk